## Slide 1: 3dfx Rampage

## Slide 2: Rampage
THE developer’s reference platform, and the most powerful graphics platform available for the personal computer for the year 2000.
As big a leap forward in 3D graphics for the PC as the original Voodoo Graphics

## Slide 3: Rampage Key Features
17M Triangles/s
800MP/s fill rate
4 fully featured pixels per clock
Multi-sample antialiasing
Enhanced 3dfx T-Buffer technology
Integrated geometry co-processing
Radically new 3D features
AGP 4X with Execute Mode
16MB to 128MB frame buffer
New, full featured video architecture

## Slide 4: Rampage
More Pixels
  Fill rate is the most important factor for real-time 3D
  800 MPixels/sec
  Single chip offers higher fill rates than 2-way Napalm SLI
Photo-realistic Pixels
  Up to 8-textures per pixel w/o multi-pass rendering
  Greater than 32-bit pixel rendering
  Multi-sample antialiasing
  Enhanced T-Buffer technology
Optimized Geometry
  Balance geometry load with CPU
  Enable developer differentiation

## Slide 5: So what will it look like?
Enables complex, realistic scenes
  250k triangles per frame
  8 textures per pixel
  Huge amounts of textures (over 100MB)
  Full-scene, multi-sample AA
  HyperColor
  @ 60 frames per second

## Slide 6: Rampage Performance
800 MPixels/sec
  16-bit, bilinear filtered, single textured, 24-bit compressed textures w/fog
400 MPixels/sec
  16-bit, bilinear filtered, dual textured, 24-bit compressed textures w/specular and fog
200 MPixels/sec
  16-bit, bilinear filtered, quad textured, 24-bit compressed textures, 4-sample AA, w/specular and fog
100 MPixels/sec
  32-bit, bilinear filtered, 8-textured, 24-bit compressed textures, 4-sample AA, w/specular and fog

## Slide 7: Bandwidth Engine
128-bit memory controller
200+ MHz DDR SG/SDRAM
16-128MB of local frame buffer memory
100% support for AGP 4X including execute mode & fast host writes
Arbitrary Render Targets (P-Buffers, etc.)
  Rendered image can be used as texture
Internal crossbar architecture for additive memory bandwidth
  Improves memory BW efficiency
6.4GB/sec frame buffer memory bandwidth (using 200 MHz DDR)
Highly efficient memory utilization, optimal fetch granularity
Intelligent look-ahead and page pre-charge
Flexible per-surface memory organization, block, tiled and linear

## Slide 8: Bandwidth Engine
Integrated AGP4x Bridge
  Full support for all AGP4X features
  Support for AGP4X SLI
    Fast Host Writes
    Execute Mode
Up to 4-way SLI
  1 Rasterizer: 800+ Mpixels/sec
  2 Rasterizers: 1.6+ GPixels/sec
  4 Rasterizers: 3.2+ GPixels/sec
  Optimized raster pattern for SLI
    Greatly improved SLI efficiency

## Slide 9: RezN8 Texture Array
Up to 8 textures w/o multipass rendering
  8-way associativity
  Many patents (10+)
  High precision iterators
  Register based combiners
  Out-of-order texturing
  Texture Recirculation & recursion
    True Bump Mapping w/environment mapping
Programmable Filter Kernel (per texture)
  Bilinear
  Trilinear
  Programmable Anisotropic - up to 128-tap (16 trilinear x 8 sample in single pass)

## Slide 10: RezN8 Texture Array
Enhanced T-Buffer
  Sub-sample, full scene antialiasing
  Motion blur
  Depth of field
  Soft shadows
  Soft reflectance
Increased sampling size of up to 8, 16 samples with 2-way
  At 16 samples you achieve “Bug’s Life” quality

## Slide 11: RezN8 Texture Array
Multiple Patents-pending texture bandwidth amplifier
  Patented 2-stage architecture
  Very high efficiency w/o huge die area penalty
  Supports compressed & uncompressed textures
  64-entry
Flexible Texture compression engine
  Supports Microsoft texture compression
  Supports 3dfx patent-pending texture compression
Color Combine Unit
  Highly programmable
  Virtually N x N or N + N color combine modes
  Unique color iterator per texture
  Iterate specular w/o performance cost when multi-texturing

## Slide 12: RezN8 Texture Array
Radically advanced Bump Mapping
  High quality bump mapping: ReN8 Texture Array bump mapping track the light in true 3D rather than DX7’s 2D
  Dynamic bump mapping: using 3 or more textures
  Smooth bump mapping: Smooth seams across polygon edges.
Procedurally generated effects
  The more textures the better
  Having flexible recursive texturing is critical, and makes the effects look substantially better.
  The generality of the math unit allows it to dynamically generate particle system effects (not just play back of movies or CPU generated data) such as fire and explosions.

## Slide 13: Coherent Pixel Engine
Sample Engine antialiasing
  Sub-sample, full-scene antialiasing
  No performance penalty for multi-textured cases
  No order requirement
  No API changes
  SGI Infinite Reality-like
4 fully featured pixels per clock
16-bit or 32-bit color rendering to frame buffer
16-bit or 24-bit integer or floating point depth buffer
8-bit stencil buffer
Patent-pending frame buffer cache
  Reduce off-chip frame buffer bandwidth

## Slide 14: Rampage Graphics Pipeline
All internal calculations at 52-bits precision
13 bits signed per component
Iterated alpha
OverBright lighting
  Reduces the darkening inherent in multi-texture rendering.

## Slide 15: Geometry
Optimized Geometry Acceleration w/Viewport transform & Clipping
  Reduces CPU requirements by moving the W reciprocal calculations into hardware.
  Performs viewport transformation in HW
  Performs color and texture coordinate scaling to reduce driver overhead.
  Truly balanced solution optimizing cost of subsystem vs. CPU performance
What the developers have been asking for
  Move transform and clipping functions to hardware
  Leave lighting on the host side
Provides developers with improved performance and the ability to differentiate through lighting and multiple textures

## Slide 16: Setup Engine
17M triangles per second peak
Fully pipelined, floating point triangle setup
IEEE SP Floating Point
Early guardband primitive rejection
Accepts fully featured D3D TL verticies
Patented triangle-filling technique
Support for strips, fans and meshes
Backface culling
Floating point sub-pixel correction
Supports 8 simultaneously active clip regions
Support for OpenGL lines (wide & stippled) with support for AA lines.

## Slide 17: Delivered Performance
Frame rate on Unreal @ 16-bit color with multi-sample AA @ 1600x1200 (7.68M texels @ DC 2.2)
Banshee
Voodoo3
Rampage
1 fps
4.7 fps
47.3 fps
10x Faster!

## Slide 18: Rampage Video Engine
New Video architecture ... from the ground up
350 MHz 10-bit RAMDAC with independently programmable gamma
VIP Port 1.1 w/2.0 extensions - including ability to support HDTV resolution data rates
  1920 x 1080 @ 60i
  Support for industry standard encoders & decoders.
  Support for industry standard MPEG-2 decoders.

## Slide 19: Rampage Video Engine
Motion Compensation
8 tap X, 4 tap Y video filtering w/programmable coefficients.
De-flickering
Bob, Weave & adaptive de-interlacing
Scaling
Adaptive Cross Fading
VBI support
Flat Panel Support w/external transmitter

## Slide 20: Rampage 2D
Worlds fastest 2D
Derived from Voodoo3 2D
Optimized to take advantage of Rampage’s massive memory bandwidth
Support for full AGP execute modes
Delivers highest performance available

## Slide 21: Physical Design
.18 micron
200 MHz typical frequency
~8W
~18M transistors

## Slide 22: AIC Configurations
1-way Rampage
  32 / 64 / 128MB
  800MP/s
2-way Rampage
  64 / 128MB
  1.6GP/s
4-way Rampage
  128 / 256MB
  3.2GP/s

## Slide 23: Rampage Development
Rampage is the first product at 3dfx to be developed via emulation
Reduces time to market and increases confidence in the architecture
Provides robust
  First silicon
  Initial drivers
Emulation has proven invaluable to this development
Most blocks emulated and functional at this time

## Slide 24: Rampage Schedule
Product schedule
  A0 TO 10/13/99
  Samples 02/08/00
  Qual units 03/01/00
  Pilot production 04/01/00
  WHQL 04/01/00
  Production 04/15/00
This is a conservative schedule based on the fact that this is a “from gate zero” new design